## Slide 1
Encryption + privacy
for synthetic grids
How threshold encryption works
with BNP and differential privacy
2023 threshold protocol implemented
Synthetic-grid comparison results
Notes: Selected 2023 Journal of Cryptology paper by Christian Mouchet, Elliott Bertrand and Jean-Pierre Hubaux: https://doi.org/10.1007/s00145-023-09452-8. Actual Lattigo v6.2.0 research implementation, simulated colocated roles, not a production security deployment. Cover artwork retained from prior deck (ImageGen conceptual residential grid).

## Slide 2
How the protections work together
Encryption protects computation. Calibrated noise protects the released statistics.
2
1
Meters compute statistics
The prototype simulates local meter roles on one machine.
2
Noise enters before decryption
A calibrated protocol protects the aggregate.
3
The server adds encrypted values
Its cryptographic interface uses the public key only.
4
Three authorities cooperate to decrypt
A quorum combines partial decryptions.
5
The model generates voltages
Synthetic loads pass through AC power flow.
Gaussian fitting works now. BNP testing uses direct sums and a trusted noise service.
Notes: Implemented Gaussian fitter: dpvolt/secure_agg.py fit_class, new dpvolt/threshold_agg.py and threshold_mhe/main.go. Noise enters before encryption. Threshold shares never reconstruct a complete key. Application authentication/authorization remains future work. BNP is implemented only for direct sums, using an independent trusted uniform-noise service. Fixed-grid power flow is customer-DP post-processing, not topology privacy. https://doi.org/10.1007/s00145-023-09452-8

## Slide 3
What the 2023 paper adds
Thresholdize creates secret shares. Combine prepares any committed quorum to decrypt.
3
Property | Previous Paillier | New research backend
Decryption authority | One complete private key | Any 3 of 5 authorities
Encrypted arithmetic | One scalar per ciphertext | Packed BGV vectors
Authority availability | Key holder must be available | Two may be absent at start
Released-output privacy | Depends on added noise | Still depends on added noise
The change is shared control and batching. The privacy budget stays separate.
Notes: https://doi.org/10.1007/s00145-023-09452-8 ; https://pkg.go.dev/github.com/tuneinsight/lattigo/v6/multiparty . Paper published 2023, preprint 2022/780. Semi-honest setting. Implementation uses degree-two Shamir sharing of every authority component, public-key generation, Combine and collective key-switch-to-zero. No full secret-key reconstruction. All ten possible 3-of-5 quorums tested on fresh ciphertexts/keys. Mid-round dropout/retry is not supported. Do not infer 128-bit security from the parameter choices. https://github.com/tuneinsight/lattigo/security

## Slide 4
Encryption and output privacy
BNP can satisfy DP itself. Gaussian DP and BNP are alternative noise mechanisms here.
4
Noise mechanism | No encryption | Paillier | Threshold BGV
None | No output DP | No output DP | No output DP
Gaussian DP | (0, 0.01) ideal DP | Same ideal DP | Same ideal DP
BNP uniform noise | (0, 0.01) ideal DP | Same ideal DP | Same ideal DP
All nine conditions compared. Encryption changes access to inputs, not ε or δ.
BNP uses a trusted noise service. Finite-precision DP remains unproved.
Notes: Measured data: results/threshold_20261005/metrics.json. Reproduce with run_threshold_comparison.py. Privacy unit: replace one reading, one meter, one time. Public meter clipping [0,20] kW, sensitivity 20 kW. Uniform bound 1000 kW gives (0,.01) for ideal continuous scalar sum. Gaussian sigma 797.8637 kW matches that guarantee by total variation. These are illustrative stress settings, not standards-approved parameters. Encryption-only has no nontrivial output DP. The trusted BNP service can know exact aggregate by subtracting its noise and is excluded from the DP adversary. Gaussian assumes all reporting meters contribute independent hidden noise. https://csrc.nist.gov/pubs/sp/800/226/final

## Slide 5
Noise cost at the same privacy budget
One meter reading, ε = 0 and δ = 0.01. Lower raw RMSE means less distortion.
5
Chart: Raw load RMSE (kW)
| No noise | Gaussian DP | BNP
Raw RMSE | 0 | 794.2753 | 580.6718
BNP minus Gaussian: -213.6 kW. 95% CI [-222.1, -205.1].
30 noise trials. The encryption variants preserve this utility within encoding error.
Notes: Measured data: results/threshold_20261005/metrics.json. Reproduce with run_threshold_comparison.py. Bars show means of trial RMSE, not theoretical standard deviations. The displayed paired interval covers 30 seed-paired trial differences. Utility trials use plaintext-equivalent mechanism after checking real encryption for first trial of every condition. No-noise zero error has no output DP, so it is not a privacy competitor. BNP theoretical raw RMSE 577.3503 kW; Gaussian 797.8637 kW. Encryption does not reduce DP noise. All inputs synthetic; inference is conditional on this feeder.

## Slide 6
Voltage quality after clipping
Noisy loads are clipped to public [0,200] kW bounds before AC power flow.
6
Chart: Voltage magnitude RMSE (pu)
| No noise | Gaussian DP | BNP
Voltage RMSE | 0 | 0.096538 | 0.096396
Clipped outputs: Gaussian 89.9%; BNP 90.3%.
No clear voltage advantage: the paired 95% interval includes zero. Both errors are large.
Notes: Measured data: results/threshold_20261005/metrics.json. Reproduce with run_threshold_comparison.py. 91 load rows, six time snapshots, 96 retained nodes. All measured power flows converged. RMSE averages voltage magnitudes against the publicly clipped noise-free reference. Convergence does not establish acceptable operational accuracy. 95% intervals: {"Gaussian":{"mean":0.09653808372874013,"ci95":[0.09426700194279077,0.0988091655146895]},"BNP":{"mean":0.09639563536205209,"ci95":[0.09360639089527283,0.09918487982883135]}}. Paired BNP minus Gaussian interval: {"mean":-0.00014244836668805873,"ci95":[-0.0038065736198863286,0.0035216768865102112]}. Public clipping is ideal DP post-processing but changes utility. These are direct-sum experiments, distinct from synthetic-model fitting.

## Slide 7
Measured full-feeder encryption cost
Same 91 rows and six time samples. Each condition performs real cryptography once.
7
Chart: Elapsed seconds
| No noise | Gaussian DP | BNP
Paillier | 97.8734 | 92.4962 | 95.5944
Threshold BGV | 21.9396 | 21.9212 | 21.6827
BGV includes fresh setup for every bus. Network transfer is not measured.
These implementations use different precision and security parameters.
Notes: Measured data: results/threshold_20261005/metrics.json. Reproduce with run_threshold_comparison.py. Each bus has ten meter contributions and an extra noise-service contribution, zero outside BNP. Paillier: 6006 scalar ciphertexts, one key setup outside timed releases; key setup is separately recorded. BGV: 1001 packed ciphertexts across 91 fresh key epochs, setup and process overhead included in wall time. Thus this is observed implementation cost, not security-equivalent algorithm speedup. Serial workers=1. Windows single-machine run; no LAN overhead or production hardening. No timing confidence interval from this single run.

## Slide 8
Batching and parallel processing
Matched microbenchmark: ten meters, 96 values each, three fresh runs per backend.
8
Chart: Mean elapsed seconds
| Paillier | BGV serial | BGV 4 workers
Mean elapsed time | 15.0049 | 0.24808 | 0.19893
960 → 10
ciphertexts for
the same input
vector workload
Packing reduces ciphertext count. Parallel speed depends on workload and overhead.
Notes: Measured data: results/threshold_20261005/metrics.json. Reproduce with run_threshold_comparison.py. Three raw elapsed measurements per condition: {"Paillier":[15.151837400044315,15.09007920010481,14.77280969999265],"BGV serial":[0.2637838999507949,0.24166110006626695,0.23880629998166114],"BGV 4 workers":[0.19117550004739314,0.20760999992489815,0.19800890004262328]}. Count reduction is scalar Paillier vs one packed BGV ciphertext per meter, not a 96-fold runtime claim. BGV supports 16384 slots but only 96 used in this benchmark. 4 worker goroutines parallelize independent encryptions; authority operations remain serial. Fresh threshold setup included, Paillier setup separate. Different precision and security settings. Serialized payload can grow even with fewer ciphertexts.

## Slide 9
Authority dropout and meter dropout
Three decryption authorities are enough. Missing customer readings still change the result.
9
Chart: Missing-load RMSE (kW)
| 0% | 20% | 40% | 60% | 80%
Missing-load RMSE | 0 | 9.5745 | 17.4033 | 24.5283 | 31.2465
3 of 5
All 10 valid
quorums tested
on fresh releases
At 50% meter loss, unadjusted Gaussian δ rises from 0.0100 to 0.0141.
Notes: Measured data: results/threshold_20261005/metrics.json. Reproduce with run_threshold_comparison.py. Quorum correctness tested by verify_threshold.py. Fewer than three or duplicate/invalid identities refused. This is pre-committed authority availability, not a tested network recovery mechanism. Missing-load chart is calculated from surviving synthetic meters without noise; no imputation/rescaling. Delta curve analytic at epsilon0 assuming all survivors independent and honest: effective sigma=original sigma sqrt(k/10). Survivor compensation restores nominal variance, not signal. Missing profile data and dishonest meters require separate handling.

## Slide 10
The existing model fitter now uses BGV
The new backend runs both encrypted releases: class means and clipped covariance entries.
10
16.04 s
Measured full-feeder
Gaussian model fit
91 load rows, 910 simulated meters
45 days, four time samples
Three classes, six encrypted rounds
Mean difference: 8.45e-6
Covariance difference: 9.14e-6
Differences compare with the same noise in plaintext. BNP model fitting is still future work.
Notes: Measured data: results/threshold_20261005/metrics.json. Reproduce with run_threshold_comparison.py. Fit settings epsilon=50,delta=1e-5,public synthetic load bounds [.0001,1]pu,T4,45days. This is an integration smoke test, not the eps0 direct-sum comparison. Errors measured in log-load mean and log-load covariance units. Paired plaintext reference uses same RNG to isolate quantization. Earlier Paillier result215.54s used a different archive, so no matched model-fit speedup is asserted. Data remain proportional simulated customers. BNP sum primitive is implemented, but joint BNP mean/covariance privacy accounting is not.

## Slide 11
Privacy guidance and remaining limits
NIST SP 800-226 guides the evaluation. It does not certify this prototype.
11
Requirement | Current evidence or limit
Privacy unit and budget | One reading per meter; ε = 0, δ = 0.01 in the comparison
Noise and trust | Honest Gaussian contributors; trusted BNP noise service
Repeated releases | Offline trials only; a deployment needs composition accounting
Cryptographic security | Real BGV operations; colocated roles and unaudited flooding
Finite precision | Encoding error tested; implemented DP proof still required
No claim of NIST compliance, certified 128-bit security or full-customer privacy.
Notes: https://csrc.nist.gov/pubs/sp/800/226/final ; https://github.com/tuneinsight/lattigo/security . NIST 2025 evaluation guidance motivates adjacency, bounded contribution, mechanism, trust model and accounting disclosures; no universal epsilon recommendation is inferred. This remains research. Experimental parameters LogN14, LogQ55+55,LogP55,plaintext1099511922689,scale1e6,flooding sigma2^40. No derived decryption leakage bound or independent lattice estimator assessment. Fresh epochs avoid exposed retry endpoints but do not prove full protocol security. Authenticated distributed services, malicious-share verification and persistent budget control remain absent.

## Slide 12
What this contributes to your research
A working threshold-encryption extension with measured costs and explicit privacy assumptions.
12
Implemented
Packed threshold BGV
Gaussian private model fitting
BNP encrypted direct sums
Matched utility and dropout graphs
Needed for a stronger paper
Dealer-free bounded-noise protocol
A finite-precision privacy proof
Independent customer profiles
Distributed adversarial evaluation
Novelty should rest on a new proved method or finding. “First to combine” is unverified.
Notes: Selected foundation: https://doi.org/10.1007/s00145-023-09452-8. The implemented contribution is an integration and evaluation, not an independent cryptographic invention or established first-in-CPS claim. Prior literature already combines encryption and differential privacy in cyber-physical applications. Future BNP distributed sampling must justify exact joint distribution and collusion assumptions; adding arbitrary uniform shares is insufficient. Full-customer trajectories require adjacency and privacy composition beyond this event-level comparison.